Manual use of Quick electric windlass

All Beneteau and Jeanneau boats with Quick electric windlasses have a lock screw to prevent manual operation. The rep said that they have to drill a hole and add a bolt that block the use of the windless manually; it prevents the ratchet lever from laying against the teeth. Didn't know why and Beneteau doesn’t know why, but that's how it is. AND it is not documented anywhere! Once you remove the bolt, the instruction in the manual are correct. Basically, you just flip that little rubber covered switch on the port side, which locks in that ratchet lever. Use the winch handle to loosen the clutch (the center hole), put the winch handle in the outside hole making sure to push in the little pin in, and start cranking